## Slide 1: Astronomical Data Archives Workshop
August 2019, AAO/MQ Sydney
Presented by Greg Sleap, Curtin University/MWA
Notes: Housekeeping: bathrooms, emergency exits….

## Slide 2: About the MWA
Operating since mid 2013
International collaboration of 20 led by Curtin University
One of four SKA Precursor telescopes
70-300 MHz, 30.72 MHz instantaneous b/w
256 dual polarisation tiles (128 at a time)
32 PB of raw voltages & visibility data
Image: credit Natasha Hurley-Walker/GLEAM. Foreground image John Goldsmith

## Slide 3: About the MWA
Notes: >20 partners from half a dozen countries: Aus, USA, China, Japan, Canada, NZ

## Slide 4: Services
Telescope operations
Archive of MWA Data
  Raw correlator visibilities
  High time resolution voltages
Pre-processing
  RFI flagging
  Calibration
MWA ASVO portal (Public and proprietary)
  Search / Convert / Pre-process / apply calibration / Download correlator data
  VO interfaces (TAP)
  Command-line client
Single sign on via AAF/eduGAIN/ORCID/UnitedID
MWA Project services
  Wiki / Mailing lists / Collaboration management

## Slide 5: MWA Data Flow (now)

## Slide 6: MWA Architecture
MRO

## Slide 7: Data Archive
32+ PB stored
34,000,000+ files
SGI (HPE) DMF HSM
Ingest at up to 80 TB per day
POSIX-based archive software (NGAS)
1.5 PB disk cache
3 PB of “zero-watt” disk storage
40 PB out of 63 PB of robotic tape library 7 – 10 TB per tape
x2 – duplicated libraries for redundancy
Notes: The data is then sent alllll the way to Perth using the NBN network, and gets stored at the Pawsey supercomputer where astronomers can access it. We have 31 petabytes of data….which is over 7 million DVDs’ worth !

## Slide 8: MWA ASVO

## Slide 9: MWA ASVO Architecture
Workers
Workers
VO services
Web services
Web Site
Web clients
API clients
TAP clients
TAP db
MWA ASVO db
Worker
Servers
Job Queue
API
Data
Downloads
MWA Archive
Staging/Pre-processing
MWA metadata db

## Slide 10: MWA Software Stack
Ubuntu / Centos / SLES / RHEL
Telescope operations and M&C
  Python 2.7
  Apache2
  Postgresql 10
  Java/Raspbian/Icinga/Observium/graphite, etc,etc
  On site and AWS
Data transport and archive ingest
  Python 2.7
  NGAS
Pre-processing
  Python 2.7
  C/C++, CUDA, MPI

## Slide 11: MWA Software Stack
Identity Management & project services
  Confluence wiki
  Mailman3 + Postorius + Hyperkitty
  COmanage
  pyFF
  SATOSA proxy
  SimpleSAMLphp
  Postgresql 9.6
  Nginx
  Docker
  VMWare

## Slide 12: MWA Software Stack
MWA ASVO
  Python 3.6
  aiohttp
  jinja2
  asyncpg
  pySAML
  pyvo
  Postgresql 9.6
  RabbitMQ
  CASADA VO Tools (Tomcat)
  Docker
  Django

## Slide 13: Challenges
Multiple sites to manage: MRO, Curtin, Pawsey, AWS
Relationship management: Pawsey, CSIRO, Curtin & AARNet
Menagerie of hardware, grown organically
Aging hardware
Pawsey tape system staging & reliability
HPE support for DMF/cxfs limited to old SLES 12 (~2014) 
FE nodes are an OLD SLES (v11!)
Data management- ‘cold’ vs ‘hot’ data
Storing raw data vs science data (flexibility vs efficiency)
Pawsey Monthly maintenance
Even with fat pipes, moving large data volumes is hard
Lots of existing Python 2.7 code to migrate
Shifting focus from MWA project to public users
More data quality metrics; barriers to entry

## Slide 14: Future work…
Improved VO services (TAP, SCS) and better web search
Minimise metal! Migrate all non-data intensive servers to AWS
  Web servers / VO / Databases / Identity Management / etc
Migrate to latest NGAS version
Commission new FE nodes and storage at Pawsey
Standardise more on software/hardware where possible
Increased allocation in Pawsey (manage a cap)
Data lifecycle management
Improved download service
Migrate all Python 2.x code to Python 3.x
Single sign on integration with rest of ASVO nodes
Astroquery implementation
Move to 256 tiles (4x correlator data rate, 2x voltages)
Move to using 100 Gbps link and Curtin cache MWA transport
Enable MWA ASVO to use the 3PB of cache at Curtin
Investigate RFI flagging jobs using AWS
More work on FAIR / DOI

## Slide 15: MWA Future

## Slide 16: Thank you
Greg Sleap
MWA Data Manager
greg.sleap@curtin.edu.au
http://www.mwatelescope.org https://asvo.mwatelescope.org
@mwatelescope
Murchison Widefield Array
We acknowledge the Wajarri people as the traditional owners of the MRO site.